## Slide 1: I-VT Algorithm
Sara Aleskerova
Lilit Dulyan
Advanced Eye Tracking Workshop
25-26 October, 2018

## Slide 2: Algorithms for Fixation and Saccade Detection
  Salvucci, D. D., & Goldberg, J. H. (2000).
  Identifying fixations and saccades in eye-tracking protocols. In Proceedings of the symposium on Eye tracking research & applications

## Slide 3: I-VT
is a velocity-based method that separates fixation and saccade points based on their point-to-point velocities
xn, yn
Xn+1, yn+1
Xn-1, yn-1

## Slide 4: Velocity Threshold
The longer the distance between two points, the higher is the velocity
Otero-Millan et al. (2008) Saccades and microsaccades during visual fixation, exploration, and search: Foundations for a common saccadic generator

## Slide 5: What is velocity?
Distance between 2 points
Time to travel from 1 point to the other
Velocity
Distance
Time
=

## Slide 6: Distance
Distance between 2 points A and B is the Euclidean distance

## Slide 7: What is velocity?
Distance between 2 points
Time to travel from 1 point to the other
Velocity
Distance
Time
=

## Slide 8: Time
Eye Link 1000 Hz
In 1 sec: 1000 samples
What is the duration of 1 sample in seconds?
Answer: 0.001
Time
X coord
Y coord

## Slide 9
Velocity
Euclidean distances in degrees
Time in seconds
=
Velocity in degrees per second

## Slide 10: Visual angle
http://wekoenig.de/DissWK/KoenigDissertation2010.htm
Distance from eyes to the screen (D)
Width of the screen (h)
Resolution of the screen
Degree of the visual angle () = 2*arctan(h/2*D) * (180/pi) tan() = (½ h) / D = h / 2*D
Since  = 2* ,
 = 2 * arctan(h / 2*D)
To find the angle in degrees, we multiply arctan by (180/pi)


½ h
½ h
D

## Slide 11
Velocity
Euclidean distances in degrees
Time in seconds
=
Velocity in deg/sec

## Slide 13: Setting a threshold
low velocities for fixations (i.e., <100 deg/sec)

## Slide 15: Not every point is a fixation
Minimal number of points (samples) to consider them a fixation
Let’s say it is 4
Fixations are detected!

## Slide 16: Questions?

## Slide 17: Coding time

## Slide 18: Last fixation
Cluster of fixations > minlength
Cluster of fixations < minlength